## Slide 1: CS 3700 Networks and Distributed Systems
Inter Domain Routing
(It’s all about the Money)
Revised 8/20/15

## Slide 2: Network Layer, Control Plane
Function:
  Set up routes between networks
Key challenges:
  Implementing provider policies
  Creating stable paths
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 3: ASs, Revisited
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 4: AS Numbers
Each AS identified by an ASN number
  16-bit values
  64512 – 65535 are reserved
Currently, there are > 20000 ASNs
  AT&T: 5074, 6341, 7018, …
  Sprint: 1239, 1240, 6211, 6242, …
  Northeastern: 156
  North America ASs  ftp://ftp.arin.net/info/asn.txt

## Slide 5: Inter-Domain Routing
Global connectivity is at stake!
  Thus, all ASs must use the same protocol
  Contrast with intra-domain routing
What are the requirements?
  Scalability
  Flexibility in choosing routes
    Cost
    Routing around failures
Question: link state or distance vector?
  Trick question: BGP is a path vector protocol

## Slide 6: BGP
Border Gateway Protocol
  De facto inter-domain protocol of the Internet
  Policy based routing protocol
  Uses a Bellman-Ford path vector protocol
Relatively simple protocol, but…
  Complex, manual configuration
  Entire world sees advertisements
    Errors can screw up traffic globally
  Policies driven by economics
    How much $$$ does it cost to route along a given path?
    Not by performance (e.g. shortest paths)

## Slide 7: BGP Relationships
Customer
Provider
Customer pays provider
Peer 1
Peer 2
Peer 3
Peers do not pay each other
Peer 2 has no incentive to route 1 3
Customer
Customer
Provider

## Slide 8: Tier-1 ISP Peering
AT&T
Centurylink
XO Communications
Inteliquent
Verizon Business
Sprint
Level 3

## Slide 10: Peering Wars
Reduce upstream costs
Improve end-to-end performance
May be the only way to connect to parts of the Internet
You would rather have customers
Peers are often competitors
Peering agreements require periodic renegotiation
Peer
Don’t Peer
Peering struggles in the ISP world are extremely contentions, agreements are usually confidential

## Slide 11: Two Types of BGP Neighbors
IGP
Exterior routers also speak IGP
eBGP
eBGP
iBGP
iBGP

## Slide 12: Full iBGP Meshes
Question: why do we need iBGP?
  OSPF does not include BGP policy info
  Prevents routing loops within the AS
iBGP updates do not trigger announcements
eBGP
iBGP

## Slide 13: Path Vector Protocol
AS-path: sequence of ASs a route traverses
  Like distance vector, plus additional information
Used for loop detection and to apply policy
Default choice: route with fewest # of ASs
110.10.0.0/16
AS 1
AS 2
130.10.0.0/16
AS 3
120.10.0.0/16
AS 4
AS 5
120.10.0.0/16: AS 2  AS 3  AS 4
130.10.0.0/16: AS 2  AS 3
110.10.0.0/16: AS 2  AS 5

## Slide 14: BGP Operations (Simplified)
Establish session on TCP port 179
Exchange active routes
Exchange incremental updates
AS-1
AS-2
BGP Session

## Slide 15: Four Types of BGP Messages
Open: Establish a peering session.
Keep Alive: Handshake at regular intervals.
Notification: Shuts down a peering session.
Update: Announce new routes or withdraw previously announced routes.
announcement = IP prefix + attributes values

## Slide 16: BGP Attributes
Some attributes used to select “best” path
  LocalPREF
    Local preference policy to choose most preferred route
    Overrides default fewest AS behavior
  Multi-exit Discriminator (MED)
    Chooses peering point for your network
    Specifies path for external traffic destined for an internal network
Other attributes control how routes are shared with others
  Import Rules
    What route advertisements do I accept?
  Export Rules
    Which routes do I forward to whom?

## Slide 17: Route Selection Summary
Highest Local Preference
Shortest AS Path
Lowest MED
Lowest IGP Cost to BGP Egress
Lowest Router ID
Traffic engineering
Enforce relationships
When all else fails,
break ties

## Slide 18: Shortest AS Path != Shortest Path
Source
Destination
?
?
4 hops
4 ASs
9 hops
2 ASs

## Slide 19: Hot Potato Routing
Destination
Source
3 hops total,
3 hops cost
?
?
5 hops total, 2 hops cost

## Slide 20: Importing Routes
From Provider
From Peer
From Peer
From Customer
ISP Routes

## Slide 21: Exporting Routes
To Customer
To Peer
To Peer
To Provider
Customers get all routes
Customer and ISP routes only
$$$ generating routes

## Slide 22: AS Relationships: It’s Complicated
Typical models of AS relationships are simple
  Each AS pair has exactly one relationship
  Each relationship is the same for all prefixes
Unfortunately, in practice it’s much more complicated
  Rise of widespread peering
  Regional, per-prefix peerings
  Tier-1’s being shoved out by “hypergiant” content providers
  Internet Exchange Points (IXPs) dominating traffic volume
Also, BGP is 100% insecure
  Totally possible to poison or steal routes :(