## Slide 1: CS 3700 Networks and Distributed Systems
Intra Domain Routing
Revised 9/21/16

## Slide 2: Network Layer, Control Plane
Function:
  Set up routes within a single network
Key challenges:
  Distributing and updating routes
  Convergence time
  Avoiding loops
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 3: Internet Routing
Internet organized as a two level hierarchy
First level – autonomous systems (AS’s)
  AS – region of network under a single administrative domain
  Examples: Comcast, AT&T, Verizon, Sprint, etc.
AS’s use intra-domain routing protocols internally
  Distance Vector, e.g., Routing Information Protocol (RIP)
  Link State, e.g., Open Shortest Path First (OSPF)
Connections between AS’s use inter-domain routing protocols
  Border Gateway Routing (BGP)
  De facto standard today, BGP-4

## Slide 4: AS Example
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 5: Why Do We Have ASs?
History – the Internet started as a network of networks
Routing algorithms are not efficient enough to execute on the entire Internet topology
Different organizations may use different routing policies
Allows organizations to hide their internal network structure
Allows organizations to choose how to route across each other (BGP)
Easier to compute routes
Greater flexibility
More autonomy/independence

## Slide 6: Routing on a Graph
Goal: determine a “good” path through the network from source to destination
What is a good path?
  Usually means the shortest path
  Load balanced
  Lowest $$$ cost
Network modeled as a graph
  Routers  nodes
  Link  edges
    Edge cost: delay, congestion level, etc.
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 7: Routing Problems
Assume
  A network with N nodes
  Each node only knows
    Its immediate neighbors
    The cost to reach each neighbor
How does each node learn the shortest path to every other node?
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1

## Slide 8: Intra-domain Routing Protocols
Link state
  Open Shortest Path First (OSPF), based on Dijkstra
  Each network periodically floods immediate reachability information to all other routers
  Per router local computation to determine full routes
Distance vector
  Routing Information Protocol (RIP), based on Bellman-Ford
  Routers periodically exchange reachability information with neighbors

## Slide 9: Outline
Link State Routing
  OSPF
  IS-IS
Distance Vector Routing
  RIP

## Slide 10: Link State Routing
Each node knows its connectivity and cost to direct neighbors
Each node tells every other node this information
Each node learns complete network topology
Use Dijkstra to compute shortest paths

## Slide 11: Flooding Details
Each node periodically generates Link State Packet
  ID of node generating the LSP
  List of direct neighbors and costs
  Sequence number (64-bit, assumed to never wrap)
  Time to live
Flood is reliable (ack + retransmission)
Sequence number “versions” each LSP
Receivers flood LSPs to their own neighbors
  Except whoever originated the LSP
LSPs also generated when link states change

## Slide 12: Dijkstra’s Algorithm
Step | S | B | C | D | E | F
0 | A | 2, A | 5, A | 1, A | ∞ | ∞
1 | AD |  | 4, D |  | 2, D | ∞
2 | ADE |  | 3, E |  |  | 4, E
3 | ADEB |  |  |  |  | 
4 | ADEBC |  |  |  |  | 
5 | ADEBCF |  |  |  |  | 
A
B
C
D
E
F
5
2
3
5
2
1
1
2
3
1
Initialization:
S = {A};
for all nodes v
if v adjacent to A
then D(v) = c(A,v);
else D(v) = ∞;
…
…
Loop
find w not in S s.t. D(w) is a minimum;
add w to S;
update D(v) for all v adjacent
  to w and not in S:
D(v) = min( D(v), D(w) + c(w,v) );
until all nodes in S;

## Slide 13: OSPF vs. IS-IS
Favored by companies, datacenters
More optional features
Built on top of IPv4
  LSAs are sent via IPv4
  OSPFv3 needed for IPv6
Favored by ISPs
Less “chatty”
  Less network overhead
  Supports more devices
Not tied to IP
  Works with IPv4 or IPv6
OSPF
IS-IS
Two different implementations of link-state routing

## Slide 14: Different Organizational Structure
OSPF
IS-IS
Area 0
Area 1
Area 2
Area 3
Area 4
Organized around overlapping areas
Area 0 is the core network
Organized as a 2-level hierarchy
Level 2 is the backbone
Level 2
Level 1
Level 1-2

## Slide 15: Outline
Link State Routing
  OSPF
  IS-IS
Distance Vector Routing
  RIP

## Slide 16: Distance Vector Routing
What is a distance vector?
  Current best known cost to reach a destination
Idea: exchange vectors among neighbors to learn about lowest cost paths
Routing Information Protocol (RIP)
Destination | Cost
A | 7
B | 1
D | 2
E | 5
F | 1
DV Table
at Node C
No entry for C
Initially, only has info for immediate neighbors
  Other destinations cost = ∞
Eventually, vector is filled

## Slide 17: Distance Vector Routing Algorithm
Wait for change in local link cost or message from neighbor
Recompute distance table
If least cost path to any destination has changed, notify neighbors

## Slide 18: Distance Vector Initialization
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
Initialization:
for all neighbors V do
if V adjacent to A
D(A, V) = c(A,V);
else
D(A, V) = ∞;
…

## Slide 19: Distance Vector: 1st Iteration
Dest. | Cost | Next
B | 2 | B
C | 7 | C
D | ∞ | 
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 3 | D
Node B
Dest. | Cost | Next
A | 7 | A
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | ∞ | 
B | 3 | B
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
8
C
D(A,D) = min(D(A,D), D(A,C)+D(C,D))
= min(∞, 7 + 1) = 8
3
B
5
B
D(A,C) = min(D(A,C), D(A,B)+D(B,C))
= min(7, 2 + 1) = 3
D(A,D) = min(D(A,D), D(A,B)+D(B,D))
= min(8, 2 + 3) = 5
2
C
4
B
3
B

## Slide 20: Distance Vector: End of 3rd Iteration
Dest. | Cost | Next
B | 2 | B
C | 3 | B
D | 4 | B
2
3
1
A
B
C
D
1
7
Node A
Dest. | Cost | Next
A | 2 | A
C | 1 | C
D | 2 | C
Node B
Dest. | Cost | Next
A | 3 | B
B | 1 | B
D | 1 | D
Node C
Dest. | Cost | Next
A | 4 | C
B | 2 | C
C | 1 | C
Node D
…
loop:
…
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) =
min(D(A, Y),
D(A, V) + D(V, Y));
if (there is a new min. for dest. Y)
send D(A, Y) to all neighbors
forever
Nothing changes, algorithm terminates
Until something changes…

## Slide 21
4
1
A
B
C
50
loop:
wait (link cost update or update message)
if (c(A,V) changes by d)
for all destinations Y through V do
D(A,Y) = D(A,Y) + d
else if (update D(V, Y) received from V)
for all destinations Y do
if (destination Y through V)
D(A,Y) = D(A,V) + D(V, Y);
else
D(A, Y) = min(D(A, Y), D(A, V) + D(V, Y));
if (there is a new minimum for destination Y)
send D(A, Y) to all neighbors
forever
1
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
D | C | N
A | 1 | A
C | 1 | B
D | C | N
A | 2 | B
B | 1 | B
Link Cost Changes,
Algorithm Starts
Algorithm Terminates
Good news travels fast
Notes: Change circles to rectangles, don’t block the text

## Slide 22: Count to Infinity Problem
Node A
Node C
DV Announcement Cache
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | C
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | C
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 6 | C
C | 1 | C
D | C | N
A | 7 | B
B | 1 | B
D | C | N
A | 8 | C
C | 1 | C
D | C | N
A | 7 | B
B | 1 | B
C has a path to A in 5 hops
Thus, D(B,A) = 6 !
However, B does not know the path is C  B  A
Bad news travels slowly
D | C
A | 5
B | 1
D | C
B | 4
C | 5
D | C
A | 7
B | 1

## Slide 23: Poisoned Reverse
Node A
Node C
DV Announcement Cache
D | C
A | ∞
B | 1
D | C
B | 4
C | ∞
D | C
A | 50
B | 1
4
1
A
B
C
50
60
Node B
Node C
Time
D | C | N
A | 4 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 5 | B
B | 1 | B
D | C | N
A | 60 | A
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
D | C | N
A | 51 | C
C | 1 | B
D | C | N
A | 50 | A
B | 1 | B
If C routes through B to get to A
  C tells B that D(C, A) = ∞
Does this completely solve this count to infinity problem?
NO
Multipath loops can still trigger the issue

## Slide 24: Link State vs. Distance Vector
 | Link State | Distance Vector
Message Complexity | O(n2*e) | O(d*n*k)
Time Complexity | O(n*log n) | O(n)
Convergence Time | O(1) | O(k)
Robustness | Nodes may advertise incorrect link costs Each node computes their own table | Nodes may advertise incorrect path cost Errors propagate due to sharing of DV tables
n = number of nodes in the graph
d = degree of a given node
k = number of rounds
Which is best?
In practice, it depends.
In general, link state is more popular.